| GH-2040ZH- GH-20120ZH | METAL LATHE |
| --- | --- |
|  | 50000766T-50000769T 50000830T-50000833T 400/50/3 |

## PARTS LIST

JPW (Tool) AG

Tämperlistrasse 5

CH-8117 Fällanden

Switzerland

Phone	+41 44 806 47 48

Fax	+41 44 806 47 58

www.jettools.com

P 50000766T-50000769T, 50000830T-50000833T   2017-01

## Table of Contents

Table of Contents	2

Bed Assembly I	3-7

Bed Assembly II	8-11

Headstock Assembly I	12-14

Headstock Assembly II	15-17

Headstock Assembly III	18-21

Headstock Assembly IV	22-24

Headstock Assembly V	25-26

Tailstock Assembly I	27-28

Tailstock Assembly II	29-30

Tool Post Assembly I	31-33

Tool Post Assembly II	34-36

Gear Box Assembly I	37-38

Gear Box Assembly II	39-41

Gear Box Assembly III	42-44

Apron Assembly I	45-48

Apron Assembly II	49-51

Apron Assembly III	52-54

Apron Assembly IV	55-56

Gear Assembly	57-58

Micro Carriage Stop Assembly	59-60

Brake Assembly	61-63

Steady Rest Assembly	64-65

Follow Rest Assembly	66-67

Safety Guard Cover	68

Parts List for Toolpost Protection Device	69

Parts List for Lead Screw Protection Device	70-71

Parts List for Lead Screw Protection Device For GH-20120ZH	72-73

Coolant & Work Light Assembly	74

Carriage Lubrication	75

Toolbox, Accessories, and Attachments	76

Electrical Components	77

Electrical Diagram	78

Electrical Components-Parts List	79

Digital Scale Units	80

Flexible Stainless Wire Woven Tube	81

## Bed Assembly　I

Bed Assembly I (for GH-20120ZH only)

## Bed Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6250B12701A-G	Splash Guard (For GH-2040ZH only)	1000	1

C6250B12701B-G	Splash Guard (For GH-2060ZH only)	1500	1

C6250B12701C-G	Splash Guard (For GH-2080ZH only)	2000	1

C6266C12701D-G	Splash Guard (For GH-20120ZH only)	3000	1

2	GB70- M8x10	Hex Socket Cap Screw (For GH-2040/60/80ZH)	M8x10	5

2a	GB70- M6x14	Hex Socket Cap Screw (For GH-20120ZH only)	M6x14	6

3	GB97.2-8	Flat Washer (For GH-2040/60/80ZH)	8	5

3a	GB97.2-6	Flat Washer (For GH-20120ZH only)	6	16

4	GB6172-M6	Hexagon thin nut (For GH-20120ZH only)	M6	2

5	C6266C01101A-G	Bed (For GH-2040ZH only)	1000	1

C6266C01101B-G	Bed (For GH-2060ZH only)	1500	1

C6266C01101C-G	Bed (For GH-2080ZH only)	2000	1

C6266C01101D-G	Bed (For GH-20120ZH only)	3000	1

6	GB5782- M20x60	Hexagon Head Bolt	M20x60	4

7	C6140W01705	Crossed Head		1

8	C6140W01706	Screw		1

9	C6140W01707	Sleeve		1

10	GB71- M10x12	Slotted Set Screw	M10x12	1

11	C6140W01709	Sleeve		1

12	GB85-M10x35	Square Set Screw	M10x35	1

12a	GB6172-M10	Hex Nut	M10	1

13	C6140W01104	Fork		1

14	GB118-8x50	Taper Pin	8x50	1

15	C6140W01710	Shaft		2

16	GB91-2x20	Split Pin	2x20	4

17	C6140W01711A	Pulling Rod		1

18	C6266C01106-G	Sleeve		1

19	GB71-M6x16	Slotted Set Screw	M6x16	1

19a	GB6172-M6	Nut	M6	1

20	C6140W01703	Hex Feed Rod (For GH-2040ZH only)		1

C6266C01703B	Hex Feed Rod (For GH-2060ZH only)		1

C6266C01703C	Hex Feed Rod (For GH-2080ZH only)		1

C6266C01703D	Hex Feed Rod (For GH-20120ZH only)		1

21	C6140W01702	Lead Screw (For GH-2040ZH only)		1

C6266C01702B	Lead Screw (For GH-2060ZH only)		1

C6266C01702C	Lead Screw (For GH-2080ZH only)		1

C6266C01702D	Lead Screw (For GH-20120ZH only)		1

22	C6140W01705	Hex Control Rod (For GH-2040ZH only)		1

C6266C01705B	Hex Control Rod (For GH-2060ZH only)		1

C6266C01705C	Hex Control Rod (For GH-2080ZH only)		1

C6266C01705D	Hex Control Rod (For GH-20120ZH only)		1

23	C6140W01724	Sleeve		1

23a	GB879-5x30	Spring Pin	5x30	2

24	C6140W01725	Sleeve		1

25	C6140W01302	Copper Sleeve		1

26	C6140W01301	Copper Sleeve		1

27	C6140W01109-G	Bracket		1

## Bed Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

28	GB70- M8x20	Hex Socket Cap Screw	M8x20	1

29	GB70- M10x70	Hex Socket Cap Screw	M10x70	1

30	GB70- M10x25	Hex Socket Cap Screw	M10x25	1

31	GB118-8x35	Taper Pin	8x35	2

33	GB2672-M6x8	Screw	M6x8	1

34	C6140W01726	Cover (serial #1601ZH0793 and lower)		1

C6266C01736	Cover (serial #1601ZH0794 and higher)		1

34a 	C6266C04A311	Label (serial #1608ZH0809 and lower)		1

C6266C04A311-1	Label (serial #1608ZH0810 and higher)		1

37	GB118-8x45	Taper Pin (For GH-2040ZH only)	8x45	8

GB118-8x45	Taper Pin (For GH-2060ZH only)	8x45	10

GB118-8x45	Taper Pin (For GH-2080ZH only)	8x45	12

GB118-8x45	Taper Pin (For GH-20120ZH only)	8x45	18

38	GB70- M10x35	Hex Socket Cap Screw (For GH-2040ZH only)	M10x35	8

GB70- M10x35	Hex Socket Cap Screw (For GH-2060ZH only)	M10x35	10

GB70- M10x35	Hex Socket Cap Screw (For GH-2080ZH only)	M10x35	12

GB70- M10x35	Hex Socket Cap Screw (For GH-20120ZH only)	M10x35	18

39	C6266C01704	Rack (For GH-2040ZH only)		1

C6266C01704	Rack (For GH-2060ZH only)		1

C6266C01704	Rack (For GH-2080ZH only)		1

C6266C01704	Rack (For GH-20120ZH only)		1

40	C6140W01719	Rack (For GH-2040ZH only)		2

C6140W01719	Rack (For GH-2060ZH only)		4

C6140W01719	Rack (For GH-2080ZH only)		5

C6140W01719	Rack (For GH-20120ZH only)		8

41	GB70- M10x85	Hex Socket Cap Screw	M10x85	2

42	C6266C01103	Gap		1

43	GB118-16x60	Taper Pin	16x60	2

44	GB70- M16x50	Hex Socket Cap Screw	M16x50	4

49	C6140W01733	Pin		1

50	GB5782- M20x80	Hexagon Head Bolt (Except For GH-20120ZH)	M20x80	8

GB5782- M20x80	Hexagon Head Bolt (For GH-20120ZH only)	M20x80	12

51	GB97.2-20	Flat Washer (Except For GH-20120ZH)	20	8

GB97.2-20	Flat Washer (For GH-20120ZH only)	20	12

52	GB85- M12x75	Set Screw	M12x75	2

53	C6266C18716-G	Bracket		1

54	GB5781-M8X25	Hex Bolt	M8X25	1

54a	GB6172-M8	Nut	M8	1

55	C6266CLRG40	Rubber Gasket (For GH-2040ZH only)		1

C6266CLRG60	Rubber Gasket (For GH-2060ZH only)		1

C6266CLRG80	Rubber Gasket (For GH-2080ZH only)		1

56	C6266CRRG	Rubber Gasket (Except For GH-20120ZH)		1

57	GB819- M5×12	Cross Recessed Countersunk Head Screw (For GH-20120ZH only)				M5×12	2

58	C6140W-01721-G	Cover (For GH-20120ZH only)		1

59	GB70- M6×10	Hex Socket Cap Screw (For GH-20120ZH only)	M6×10	10

60	C6266C18702/1650-G	Line Pipe (For GH-20120ZH only)		1

## Bed Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

61	C6266C18709	Articulating Sleeve (For GH-20120ZH only)	50x82xR100x1000	2

62	C6266C18711-G	Drag Chain Support (For GH-20120ZH only)		1

63	C6266C18710-G	Drag Chain Support (For GH-20120ZH only)		1

64	C6266C18712	Drag Chain Carriage (For GH-20120ZH only, serial #1601ZH0793 and lower)					1

C6266C18712A	Drag Chain Carriage (For GH-20120ZH only, serial #1601ZH0794 and higher)					1

65	P3	Flexible Stainless Wire Woven Tube (For GH-2040ZH only)				M33x2M30x2-1.05m	1

P3	Flexible Stainless Wire Woven Tube (For GH-2060ZH only)				M33x2M30x2-1.50m	1

P3	Flexible Stainless Wire Woven Tube (For GH-2080ZH only)				M33x2M30x2-1.65m	1

P3	Flexible Stainless Wire Woven Tube (For GH-20120ZH only)				M33x2M30x2-2.60m	1

66	GB70- M6x12	Hex Socket Cap Screw (For GH-2040/60/80/120ZH)	M6x12	3

67	D93-2-G	Tee Pipe Coupling (For GH-20120ZH only)	M33X2	1

68	C6140W18702/700-G	Line Pipe (For GH-2040ZH only)		1

C6266C18702/950-G	Line Pipe (For GH-2060ZH only)		1

C6266C18702/1200-G	Line Pipe (For GH-2080ZH only)		1

69	D93-1-G	Tee Pipe Coupling (For GH-2040/60/80ZH)	M33X2	1

70	C6140W18702/750-G	Line Pipe (For GH-2040ZH only)		1

C6266C18703/1000-G	Line Pipe (For GH-2060ZH only)		1

C6266C18703/1250-G	Line Pipe (For GH-2080ZH only)		1

71	D91-4-G	Right Angle Flange Pipe Joint (For GH-2040/60/80ZH)	M33X2	1

72	C0632-01305	Label (serial #1608ZH0809 and lower)		1

GHB1340A01301-1	Label (serial #1608ZH0810 and higher)		1

73	GB827-2x3	Rivet	2x3	4

74	ZH-SQ4	Micro Switch	LXW5-11Q1	1

Bed Assembly　II

Bed Assembly II (for GH-20120ZH only)

## Bed Assembly　II

#### Index	Part

#### No.	No.	Description	Size	Qty.

4	C6266C01105	Pulley		1

5	GB1096-10x50	Flat Key	10x50	1

6	GB71- M12x16	Slotted Set Screw	M12x16	1

7	Y132M-4TH/B3	Motor	10HP, 3PH, 400V	1

8	GB5782- M10x40	Hexagon Head Bolt	M10x40	4

9	GB93-10	Spring Washer	10	4

10	GB97.2-10	Flat Washer	10	4

11	GB6170- M20	Hex Nut	M20	2

12	GB849-20	Spheric Washer	20	2

13	C6140W01735	Taper Washer		2

14	C6140W01714	Double Bolt		1

15	C6266C01711	Shaft		1

16	C6266C01104	Motor Mounting Plate		1

17	GB75- M10x14	Slotted Set Screws (Except For GH-20120ZH)	M10x14	1

18	C6266C01107	Support (Except For GH-20120ZH)		1

19	GB70- M12x35	Hex Socket Cap Screw (Except For GH-20120ZH)	M12x35	4

20	C6266C01701-G	Cover		1

21	GB97-6	Flat Washer	6	12

GB97-6	Flat Washer (For GH-20120ZH only)	6	16

21a	GB93-6	Spring Washer	6	8

22	GB818-M6x8	Cross Head Screw (serial #1601ZH0793 and lower)	M6x8	12

GB2672-M6x8	Screw (serial #1601ZH0794 and higher)	M6x8	12

GB818-M6x8	Cross Head Screw (For GH-20120ZH only) (serial #1601ZH0793 and lower)				M6x8	16

GB2672-M6x8	Screw (For GH-20120ZH only) (serial #1601ZH0794 and higher)				M6x8	16

23	C6266C01710-G	Cover		1

24	C6266C01102A-G	Bed Stand (For GH-2040ZH only)	1000	1

C6266C01102B-G	Bed Stand (For GH-2060ZH only)	1500	1

C6266C01102C-G	Bed Stand (For GH-2080ZH only)	2000	1

24a	C6266C01108-G	Front Bed Stand (For GH-20120ZH only)	3000	1

24b	C6266C01109-G	Middle Bed Stand (For GH-20120ZH only)	3000	1

24c	C6266C01110-G	Rear Bed Stand (For GH-20120ZH only)	3000	1

25	C6266C01707-G	Cover		1

27	1440R01705	Drain Plate (Except For GH-20120ZH)		1

28	GB41- M6	Hex Nut (Except For GH-20120ZH)	M6	2

29	GB5782- M6×20	Hexagon Head Bolt (Except For GH-20120ZH)	M6×20	1

30	C6140W01723-G	Cover (For GH-20120ZH only)		1

31	C6266C01715-G	Front Splash Guard (For GH-20120ZH only)		1

32	GB70-M8X16	Cross Head Screw (For GH-20120ZH only)	M8X16	12

32a	GB97-8	Washer (For GH-20120ZH only)	8	12

34	STRIRZ-1-314	Saripe (not shown)		1

35	GB70-M6x16	Hex Socket Cap Screw (For GH-20120ZH only)	M6x16	2

36	C6266C01713-G	Coolant Tank Bracket (For GH-20120ZH only)		1

37	C6266C01712-G	Lacquer Tray (For GH-20120ZH only)		2

39	C61321723A-G	Bracket		1

40	GB70- M8x12	Hex Socket Cap Screw	M8x12	2

## Bed Assembly　II

#### Index	Part

#### No.	No.	Description	Size	Qty.

41	JET-165	JET LOGO (serial #1601ZH0794 and higher)		1

42	K990	Motor Label		1

44	GH-1640ZX18303A-G	Wiring Box		1

45	GH-1440A18304-G	Wiring Box Cover		1

46	GB818-M6x8	Cross Head Screw	M6x8	2

47	C613618302	Warning Label		1

48	GB2672-M6x20	Screw	M6x20	2

Headstock Assembly　I

Headstock Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6140W02505-G	Headstock Cover		1

2	C6140W02509	Rubber Gasket		1

3	C6140W02835	Sunk Screw		1

4	GB70-M10x40	Hex Socket Cap Screw	M10x40	8

5	GB6172-M12	Hex Flat Nut	M12	2

6	C6140W02816	Screw		1

7	GB65-M6x12	Slotted Socket Cap Screw	M6x12	4

8	C6140W02796	Braking Belt		1

9	GB867-3x8	Half Circle Rivet	3x8	3

10	C140W02503	Braking Friction Disk		1

11	C6140W02797	Shaft		1

12	C6140W02798	Braking Belt Support		1

13	GB119-6m6x25	Pin	6m6x25	1

14	C6250B02101-G	Headstock		1

15	GB5782-M20x65	Hexagon Head Bolt	M20x65	3

15a	GB97-20	Washer	20	3

16	C6140W02107	Fork		1

17	GB71-M12x14	Slotted Set Screw	M12x14	1

18	Q81-1-1.6x8x70	Spring	1.6x8x70	1

19	GB308-10	Steel Ball	10	1

20	GB818-8x40	Cross Recessed Pan Head Screws	8x40	1

21	C6140W02731	Positioning Shaft		1

22	C6140W02105	Bushing		1

23	C6250B02138	Fork		1

24	C6140W02130	Fork		1

25	C6140W02829	Fork Shaft		1

26	R51-2-20	Oil Sight Glass	20	2

27	C6140W02141-G	Front Cover		1

28	C6250B02305-38	Label (For GH-2040ZH only) (serial #1608ZH0809 and lower)	1

C6250B02305-39	Label (For GH-2060ZH only) (serial #1608ZH0809 and lower)	1

C6250B02305-40	Label (For GH-2080ZH only) (serial #1608ZH0809 and lower)	1

C6250B02305-53	Label (For GH-20120ZH only) (serial #1608ZH0809 and lower)	1

C6250B02305-65	Label (serial #1608ZH0810 and higher)		1

29	GB818-M3x5	Screw (serial #1601ZH0793 and lower)	M3x5	10

GB2672-M3x6	Screw (serial #1601ZH0794 and higher)	M3x6	10

30	GB5782-M16x80	Hexagon Head Bolt	M16x80	2

30a	GB97-16	Hexagon Head Bolt	16	3

31	C6140W02831	Nut		1

33	C6140W02832	Drain Pipe		1

34	C6140W02833	Clamping Plate		1

35	GB5782-M16x60	Hexagon Head Bolt	M16x60	1

36	C6140W02143	Slide Block		1

37	GB119-8m6x20	Pin	8m6x20	1

38	GB1099-6x22	Half Circle Key	6x22	1

39	C6140W02129	Rocker		1

40	C6140W02815	Shaft		1

41	GB1235-25x2.4	Ring Seal	25x2.4	3

Headstock Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

42	C6140W02127	Collar		1

43	GB818-M6x16	Cross Head Screw	M6x16	3

43a	GB97-6	Washer	6	3

44	C6266C02757-G	Cover		1

45	GB3452.1-38.7x3.55	Ring Seal	38.7x3.55	1

46	C6140W02836	Oil Distributor		1

47	G92-1A-10	Fitting	10	4

48	G92-1A-6	Fitting	6	2

49	GB818-M5×12	Cross Recessed Pan Head Screw	M5×12	3

50	C6140W02838	Bracket		1

51	GB819-M5×10	Cross Recessed Head Screw	M5×10	2

52	C6140W02837	Board		1

53	G92-1A-4	Fitting	4	10

54	GB818-M5×14	Cross Recessed Pan Head Screw	M5×14	2

55	C6140W02840	Combination Of Oil Sprayer		1

56	C6140W02841	Plug		1

57	SFW-02A	Oil Filter		1

58	GB78-M8×10	Hex Socket Set Screw With Cone Point	M8×10	1

59	GB73-M8×10	Slotted Set Screw	M8×10	1

Headstock Assembly II

## Headstock Assembly II

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	GB70-M10x25	Hex Socket Cap Screws	M10x25	6

2	C6250B02115	Back Flange Cover		1

3	G51-2B-170x2.65	Ring Seal	170x2.65	1

4	GB894.1-95	Circlip for Shaft	95	2

5	C6250B02772	Oil Splash Ring		1

6	6019/P5	Deep Groove Ball Bearing		1

7	C6250B02116	Sleeve		1

8	C6250B02773	Gear		1

9	C6250B02789 (2/2)	Clamping Block		1

10	C6250B02789 (2/2)	Round Nut		1

11	GB77-M10x25	Hex Socket Set Screw	M10x25	1

12	C6250B02790	Sleeve		1

13	GB893.1-150	Circlip for Bore	150	1

14	NN3020/P5	Double Row Roller Bear	100x150x37	1

15	C6250B02716	Gear		1

16	C6250B02702	Thread Sleeve		1

17	C6250B02703	Nut		1

18	GB67-M6x10	Slotted Pan Head Screw	M6x10	1

19	C6140W02715	Fixing Plate		1

20	C6250B02705	Gear		1

24	C6250B02706 (1/2)	Round Nut		1

25	C6250B02706 (2/2)	Clamping Block		1

26	234424/P5	Thrust Ball Bearing	120x150x72	1

27	C6250B02712	Sleeve		1

28	NN3024K/W33/P5	Double Row Ball Bearing	120x150x46	1

29	1440R02702	Oil Splash Ring		1

30	G51-2B-218x2.65	Ring Seal	218x2.65	1

31	GB3452.1-45x3.55	Ring Seal	45x3.55	1

32	C6250B02102A-G	Front Flange Cover		1

33	GB70-M10x25	Hex Socket Cap Screws	M10x25	6

34	GB1096-10x50	Key	10x50	1

35	C6250B02701	Spindle (D Type)		1

36	1440R02701	Cam (For D Type)		6

38	C6140W-02735	Shaft Ⅷ		1

39	GB893.1-47	Circlip for Bore	47	2

40	C6140W02739	Gear		1

41	GB1096-8x35	Key	8x35	1

42	6005/P6	Deep Groove Ball Bearing	25x47x12	2

43	C6140W02110	Sleeve		1

44	C6140W02738	Gear		1

45	C6140W02737	Braking Wheel		1

46	GB894.1-58	Circlip for Shaft	58	1

47	C6140W02765	Screw		1

48	C6140W02774	Bearing Cover		1

49	6205/P6	Bearing	25x52x15	1

## Headstock Assembly II

#### Index	Part

#### No.	No.	Description	Size	Qty.

50	C6140W02778	Gear		1

51	GB894.1-30	Circlip for Shaft	30	2

52	C6140W02784	Double Gear		1

53	C6140W02777	Shaft Ⅳ		1

54	C6140W02775	Plug		1

55	GB894.1-22	Circlip for Shaft	22	1

56	C6140W02782	Washer		2

57	C6140W02781	Gear		1

58	C6140W02306	Copper Sleeve		1

59	C6140W02783	Shaft Ⅸb		1

60	GB72-M8x16	Slotted Set Screw	M8x16	1

63	GB6172-M20	Hex Flat Screw	M20	1

64	GB97.1-20	Washer	20	1

65	GB70-M8x25	Hex Socket Cap Screws	M8x25	1

66	GB119-6m6x25	Pin	6m6x25	1

67	C6140W02824	Positioning Shaft		1

68	GB3452.1-92-20x2.65	Ring Seal	20x2.65	1

69	GB79-M8x14	Hex Socket Cap Screws	M8x14	1

70	C6140W02828	Pin Shaft		1

71	C6140W02140	Rocker		1

72	GB119-6n6x14	Pin	6n6x14	1

73	C6140W02812	Roller		1

74	C6250B02142	Rocker		1

75	C6140W02119	Sliding Block		1

76	C6250B02142	Washer		1

77	GB3452.1-20x2.65	Ring Seal	20x2.65	1

78	GB1096-12x50	Key	12x50	1

79	GB1096-16x50	Key	16x50	1

80	Q81-1-1x8x25	Spring	1x8x25	1

81	GB68-M5x12	Recessed Sunk Head Screw	M5x12	1

82	C6140W02776	Adjusting Plug		1

83	6006-2KS/P6	Both Ends Sealed Bearing		1

84	GB13871-35x51x8	Seal	35x51x8	1

85	GB70-M10x25	Hex Socket Cap Screws	M10x25	4

86	C6250B02117	Bearing Support		1

87	G51-2A-80x3.1	Ring Seal	80x3.1	1

88	C6250B02779	Shaft X		1

89	C6140W02780	Gear		1

90	C6140W02793	Fork Shaft		1

91	C6140W02133	Fork		1

92	GB894.1-25	Circlip for Shaft	25	1

## Headstock Assembly III

## Headstock Assembly III

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6140W02752 (1/2)	Round Nut		1

2	GB77-M6x6	Hex Socket Set Screw 	M6x6	1

3	C6140W02752 (2/2)	Clamping Block		1

4	B-2159	Belt		4

5	C6140W02113	Pulley		1

6	GB70-M10x25	Hex Socket Cap Screws	M10x25	4

7	C6140W02111	Bearing Support		1

8	GB3452.1-115x3.55	Ring Seal	115x3.55	1

9	BB-6208ZZ	Bearing	6208ZZ	2

10	C6140W02112	Sleeve		1

11	GB893.1-80	Circlip for Bore	80	1

12	C6140W02740	Sleeve		4

13	C6140W02749	Gear		1

14	C6140W02301	Collar		1

15	C6140W02748	Washer		2

15	C6140W02747	Washer		2

17	GB119-5x10	Pin	5x10	2

18	C6140W02746	Inner Friction Disk (forward 9 pcs and reverse 7 pcs)		16

19	C6140W02745	Outer Friction Disk (forward 8 pcs and reverse 6 pcs)		14

20	C6140W02741	Adjusting Nut		2

21	C6140W02742	Sleeve Nut		1

22	C6140W02744	Stop Pin		1

23	Q81-1-0.8x5x16	Spring	0.8x5x16	2

24	C6140W02736	Gear		1

25	C6140W02109	Sleeve		1

26	C6140W02108	Sleeve		1

27	GB894.1-40	Circlip for Shaft	40	1

28	GB1096-12x50	Key	12x50	1

29	C6140W02751	Shaft Ⅰ		1

30	GB119-12x70	Pin	12x70	1

31	C6140W02732	Lever		1

32	GB119-5x40	Pin	5x40	1

33	GB1096-12x70	Key	12x70	1

34	GB119-8x25	Pin	8x25	1

35	C6140W02733	Clamping Ring		1

36	C6140W02743	Shaft		1

37	C6140W02730	Shaft connecting Oil Pump		1

38	GB70-M6x20	Hex Socket Cap Screws	M6x20	4

39	C6140W02106	Pump Support		1

40	GB1096-4x20	Key	4x20	1

41	DB-B4	Oil Pump		1

42	C6140W02765	Bolt		4

43	C6140W02754	Bearing Cover		1

44	6035/P6	Bearing	25x62x17	1

45	C6140W02131	Sleeve		1

46	C6140W02755	Gear		1

47	C6140W02756	Gear		1

## Headstock Assembly III

#### Index	Part

#### No.	No.	Description	Size	Qty.

48	C6140W02757	Gear		1

49	C6140W02758	Gear		1

50	C6140W02114	Sleeve		1

51	C6140W02753	Shaft Ⅱ		1

52	6205/P6	Deep Groove Ball Bearing	25x52x15	1

54	C6140W02734	Bearing Support		1

55	6306/P6	Bearing	30x72x19	1

56	C6140W02727	Gear		1

57	C6250B02728	Shaft V		1

58	6307/P6	Bearing	35x80x21	1

59	C6140W02726	Cover for Shaft V		1

60	C6140W02104	Stopper for Shaft V Hole		1

61	C6140W02717	Hex Socket Cap Screws		2

62	GB6173-M16x1.5	Hex Flat Nut	M16x1.5	1

63	C6140W02759	Bearing Cover		1

64	6306/P6	Bearing		1

65	C6140W02762	Washer		1

66	C6140W02764	Gear		1

67	C6140W02302	Copper Sleeve		1

68	C6140W02763	Washer		1

69	GB894.1-35	Circlip for Shaft	35	1

70	C6140W02760	Gear		1

71	C6140W02761	Gear		1

72	GB1096-6x16	Key	6x16	1

73	C6140W02768	Gear		1

74	C6140W02769	Gear		1

75	C6140W02771	Double Gear		1

76	C6140W02770	Shaft Ⅲ		1

77	C6140W02766	Bearing Cover		1

78	6308/P6	Deep Groove Ball Bearing	40x90x23	3

79	C6250B02767	Gear		1

80	GB1099-6x22	Half Circle Key	6x22	1

81	C6140W02785	Shaft Ⅳ		1

82	C6140W02786	Gear		1

83	C6140W02787	Gear		1

84	C6140W02725	Double Gear		1

85	C6140W02750	Slide Sleeve		1

86	6005/P6	Bearing	25x47x12	1

87	C6140W02724	Inner Gear		1

88	30209	Taper Roller Bearing	45x85x19	1

89	C6140W02723	Washer		1

90	C6250B02719	Gear		1

91	C6140W02722	Connecting Plate		3

92	C6140W02721	Gear		1

93	GB1099-8x25	Half Circle Key	8x25	1

94	C6140W02720	Shaft Ⅵ		1

95	32308	Taper Roller Bearing	40x90x33	1

## Headstock Assembly III

#### Index	Part

#### No.	No.	Description	Size	Qty.

96	C6140W02718	Couer for Shaft Ⅵ Hole		1

97	C6250B02103	Stopper for Shaft Ⅵ Hole		1

98	GB3452.1-82.5x3.55	Ring Seal	82.5x3.55	1

99	C6140W02729	Plug		1

100	GB3452.1-43.7x3.55	Ring Seal	43.7x3.55	1

101	GB3452.1-54.5x3.55	Ring Seal	54.5x3.55	1

102	GB3452.1-71x3.55	Ring Seal	71x3.55	1

103	GB3452.1-65x3.55	Ring Seal	65x3.55	1

104	GB119-6x8	Pin	6x8	1

109	BB-6208	Bearing	6208	1

Headstock Assembly　IV

Headstock Assembly　IV

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6140W0HA01	Roller Chain	12.7x46	1

2	GB894.1-16	Circlip For Shaft 	16	1

3	C6140W02808	Chain Wheel		2

4	C6140W02807	Gear		1

5	C6140W02806	Sleeve		1

6	C6140W02803	Positioning Sleeve		1

7	GB819-M6x14	Cross Recessed Head Screw	M6x14	8

8	C6140W02799-G	Lever		1

9	C6140W02122-G	Lever Support		1

11	GB3452.1-20x2.65	Ring Seal	20x2.65	1

12	GB1096-5x10	Key	5x10	4

13	C6140W02805	Sleeve		1

14	GB308-10	Steel Ball	10	1

15	Q81-1-YI-1.6x8x18	Spring	YI-1.6x8x18	1

16	C6140W02802	Positioning Sleeve		1

17	GB894.1-25	Circlip For Shaft 	25	1

18	GB3452.1-12.5x1.8	Ring Seal	12.5x1.8	1

19	C6140W02804	Lever Shaft		1

20	C6140W02801-G	Lever		1

21	C6140W-02123-G	Lever Shaft		1

22	C6140W-02821-G	Washer		2

23	GB819-M5x16	Cross Recessed Head Screw	M5x16	1

24	C6140W02303	Speed Label (serial #1608ZH0809 and lower)		1

C6250B02303-2	Speed Label (serial #1608ZH0810 and higher)		1

25	C6140W02119	Slide Block		4

26	C6140W02814	Eccentric Bolt		1

27	GB6173- M12x1.25	Hex Flat Screw	M12x1.25	1

28	C6140W02126	Cam Rocker		1

29	C6140W02813	Pin		4

30	C6140W02812	Roller		2

31	GB117-6x45	Taper Pin (serial #1209ZH0608 and lower)	6x45	2

GB877-6x50	Taper Pin (serial #1301ZH0609 and higher)	6x50	2

32	C6140W02125	Rocker		1

33	C6250B02830	Connector		1

34	C6140W02124	Cam Rocker		1

35	C6140W02811	Shaft		2

36	GB117-6x30	Taper Pin (serial #1209ZH0608 and lower)	6x30	1

GB877-6x35	Taper Pin (serial #1301ZH0609 and higher)	6x35	1

37	C6140W02809	Small Gear		1

38	C6140W02791	Collar		2

39	C6140W02810	Shaft		1

40	GB119-6n6x14	Pin	6n6x14	1

41	C6140W02139	Rocker		1

42	C6140W02827	Shaft		1

43     C6250B02846	Screw		1

44	C6250B02132	Rocker		1

45	C6140W02826	Tightening Wheel		1

Headstock Assembly　IV

#### Index	Part

#### No.	No.	Description	Size	Qty.

46	C6140W02825	Pin		1

47	GB97.1-12	Washer	12	1

48	C6140W02120	Rocker		1

49	C6250B02121	Cam Rocker		1

50	C6140W02794	Positioning Disc		1

51	C6140W02802	Positioning Sleeve		2

52	GB1099-5x19	Half Circle Key	5x19	1

53	C6140W02792	Shaft		1

54	C6140W02795	Shaft		1

55	GB1099-5x19	Half Circle Key	5x19	2

56	C6140W02823	Cam		1

57	C6140W02803	Positioning Sleeve		2

58	C6140W02819	Control Shaft		1

59	C6140W02134-G	Lever Support		1

60	C6140W02822-G	Small Lever		1

61	C6140W02304	Label		1

62	GB73-M12x14	Slotted Set Screw	M12x14	1

63	GB894.1-18	Circlip For Shaft 	18	1

64	GB818-M3x6	Cross Recessed Pan Head Screw (serial #1601ZH0793 and lower)				M3x6	13

GB2672-M3x6	Screw (serial #1601ZH0794 and higher)	M3x6	13

## Headstock Assembly　V

Headstock Assembly　Ⅴ

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6250B02847-G	Rear Side Plate		1

3	GB70-M6x12	Hex Socket Cap Screw	M6x12	7

4	GB70-M6x16	Hex Socket Cap Screw	M6x16	8

5	C6266C08706	Upper Hinge		2

6	GB119-6h8x40	Pin	6h8x40	2

7	C6266C08707	Lower Hinge		2

8	C6250B02849-G	Back Cover		1

9	GB70-M6x25	Hex Socket Cap Screw	M6x25	4

10	C6250B02850-G	Cover		1

11	GB67-M6x10	Slotted Pan Head Screw (serial #1601ZH0793 and lower) M6x10	4

GB2672-M6x8	Screw (serial #1601ZH0794 and higher)	M6x8	4

11a	GB97.2-6	Washer	6	8

12	C6250B02848-G	Front Side Plate		1

13	C6140W02846-G	Plate		1

14 	GB93-6	Spring Washer	6	4

15	GHB-1340A11304-12	Warning Label (serial #1608ZH0810 and higher)		1

16	C6266C18718	Bracket		1

17	GB818-M5x6	Cross Recessed Pan Head Screw	M5x6	2

18	ZH-SQ1	Door Switch Assembly	QKS8	1

18a		Door Switch	QKS8-1	1

18b		Door Switch	QKS8-2	1

19	GB818-M4x30	Cross Recessed Pan Head Screw	M4x30	2

20	GB6172-M4	Hex Nut	M4	2

21	GB818-M4x6	Cross Recessed Pan Head Screw	M4x6	2

22	GB97-4	Washer	4	2

23	C6250B05304	Label (serial #1608ZH0810 and higher)		1

24	C6250B05305	Label (serial #1608ZH0810 and higher)		1

### Tailstock Assembly I

## Tailstock Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	GH1640ZX03105	Nut		1

2	GB70-M8x20	Hex Socket Cap Screw	M8x20	3

3	GH1840ZX03710	Lead Screw		1

4	GB1096-6x40	Plain Key	6x40	1

5	51205-25x47x15	Thrust Bearing	25x47x15	1

6	C6250B03105	Back Cover		1

7	GB1155-8	Oil Cup	8	1

8	GH1640ZX03708G	Dial		1

9	C613203711	Spring Leaf		1

10	1440R03706	Sleeve		1

11	C6140W03107A-G	Handlewheel		1

12	GB97.2-16	Flat Washer	16	1

13	GB6172-M16	Hex Flat Nut	M16	1

15	GB923-M16	Nut	M16	1

16	C6140W06766-G	Shaft		1

16a	GB895-10	Steel C-clip	10	1

16b	C6140W06765-G	Lever Sleeve		1

17	C6140W03710-G	Lever		1

18	GB117-5x20	Straight Pin	5x20	1

19	C6140W03715-G	Lever Support		1

20	C6140W03716	Washer		1

21	C6140W03717	Clamping Block		1

22	C6140W03718	Clamping Block		1

23	GB70-M12x120	Hex Socket Cap Screw	M12x120	2

25……..1860R03701A	Center Sleeve		1

29	1440R03702	Positioning Block		1

30	GB1155-10	Oil Cup	10	1

31	C6250B03101-G	Tailstock Casting		1

32	GB71-M8x25	Slotted Cylindrical End Set Screw	M8x25	2

33	GB70-M12x25	Hex Socket Cap Screw	M12x25	1

34	C063203303	Panel		1

35	GB867-3x8	Half Circle Rivet	3x8	2

36	C6140W03103	Sleeve		1

37	C6250B03704	Eccentric Shaft		1

38	GB117-6x45	Half Round Key	6x45	1

39	C6250B03103	Sleeve		1

40	GB119-8x15	Pin	8x15	1

41	C6250B03104-G	Lever Sleeve		1

42	GB117-5x40	Taper Pin	5x40	1

43……..C6250B03705-G	Lock Handle		1

Tailstock Assembly　Ⅱ

Tailstock Assembly　Ⅱ

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6140W03110	Nut		1

2	GB6171-M20x1.5	Hex Nut	M20x1.5	1

3	GB97.2-20	Flat Washer	20	1

4	GB56-M20	Hex Thick Nut	M20	1

5	C6250B03703	Pulling Rod		1

6	C6250B03102-G	Sliding Base		1

7	C063203304	Sign Plate		1

8	GB867-3x8	Half Circle Rivet	3x8	2

9	GB75-M6x16	Slotted Cylindrical End Set Screw	M6x16	4

10	GB2089-1.8x14x18	Spring (serial #1202ZH0520 and higher)		4

14	C6140W03713	Bearing Support (serial #1202ZH0520 and higher)		4

15	C6140W03714	Small Axle (serial #1202ZH0520 and higher)		4

16	607	Ball Bearing (serial #1202ZH0520 and higher)	7x19x6	4

17	C6140W03502	Wipe Plate		1

18	GB67-M6x10	Slotted Pan Head Screw (serial #1601ZH0793 and lower)	M6x10	4

GB2672-M6x10	Screw (serial #1601ZH0794 and higher)	M6x10	4

19	C6140W03503	Wipe Plate		1

20	C6140W03104-G	Clamping Block		1

21	C6250B03702	Screw		1

22	C6140W03111-G	Clamping Block		1

23	C6250B03701	Screw		1

24	GB119-5x10	Straight Pin	5x10	1

25……..GB850-20	Taper Washer	20	1

26	GB849-20	Ball Washer	20	1

27……..GB6173-M20x1.5	Hex Nut	M20x1.5	2

Tool Post Assembly　I

## Tool Post Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6250B04101-G	Slide		1

2	GB73-M10x16	Slotted Set Screw	M10x16	1

3	C6140W04503	Wipe Plate		1

4	GB819-M5x16	Cross Recessed Flat Head Screw (serial #1601ZH0793 and lower)

M5x16	19

GB2672-M5x16	Screw (serial #1601ZH0794 and higher)	M5x16	19

5	C6140W04107	Lining Plate		2

6a.	C6140W04718	Clamping Plate		1

6c	C6140W04720	Clamping Plate		1

7	GB70-M12x45	Hex Socket Cap Screw	M12x45	4

8	GB6170-M10	Hex Nut	M10	4

9	GB85-M10x35	Square Set Screw	M10x35	4

10	C6140W04501	Wipe Plate		1

11	1660R04788A	Stop Pin		1

12	1440R04507	Stop Pin Cap		1

13	GB83-M12x70	Square Cap Bolt	M12x70	1

14	GB70-M12x55	Hex Socket Cap Screw	M12x55	8

15	GB119-8x70	Pin	8x70	2

16	C6140W04713	Front Clamping Plate		1

17	C6140W04712	Locking Plate		1

18	GB119-8n6x20	Pin	8n6x20	1

19	GB68-M6x22	Recessed Sunk Head Screw	M6x22	2

20	C6140W04715	Switch Seat		1

21	C6140W04711	Line Pipe		1

22	C6140W04106	Plug		2

23	C6140W04720	Back Clamping Block		1

24	GB119-8n6x10	Pin (serial #1601ZH0793 and lower)	8n6x10	3

G38-3A-Z1/8”	Oil Plug Screw (serial #1601ZH0794 and higher)	Z1/8”	3

25	C6266C04505	Wipe Plate		1

26	C6140W04504	Wipe Plate		1

27	C6266C04756T-G	Lever Shaft (serial #1701ZH0833 and higher)		1

28	ZH-T27	Handle (serial #1611ZH0832 and lower)	598.7-KU-23	1

C6266C04757T-G	Lever Sleeve (serial #1701ZH0833 and higher)		1

29	GB70-M6x20	Hex Socket Cap Screw (serial #1611ZH0832 and lower)	M6x20	2

GB70-M6x18	Hex Socket Cap Screw (serial #1701ZH0833 and higher)	M6x18	2

30 	C6266C04756J	Fixed Seat (serial #1611ZH0832 and lower)		1

C6266C04756JA	Fixed Seat (serial #1701ZH0833 and higher)		1

31	GB70-M6x12	Hex Socket Cap Screw (serial #1611ZH0832 and lower)	M6x12	1

GB71-M5x8	Hex Socket Set Screw With Flat Point (serial #1701ZH0833 and higher)

M5x8	1

32	GB68-M3x6	Slotted Head Screw (serial #0811ZH0352 and higher)	M3x6	1

33	C6266C04758T	Locking Nut (serial #0811ZH0352 and higher)		1

34	C6266C04755J-G	Handle Seat (serial #0811ZH0352 and higher)		1

44	C6266C04718	Spring Leaf		1

45	C6266C04735G (m)	Dial		1

46 	C6250B04107	Screw Support (serial #0809ZH0351 and lower)		1

C6250B04107J	Screw Support (serial #0811ZH0352 and higher)		1

## Tool Post Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

47	GB1155-6	Oil Cup	6	1

48 	GB70- M8x20	Hex Socket Cap Screw (serial #0809ZH0351 and lower)	M8x20	4

GB70- M8x40	Hex Socket Cap Screw (serial #0811ZH0352 and higher)	M8x40	4

49	C6250B04109	Sleeve		1

50	GB1099-5x19	Half Circle Key	5x19	1

51 	C6250B04726	Shaft (serial #0809ZH0351 and lower)		1

C6250B04726J	Shaft (serial #0811ZH0352 and higher)		1

52	GB117-4x35	Taper Pin	4x35	1

53	C6266C04705	Shaft		1

54	C6266C04103	Sleeve		1

55	C6140W04301Y (m)	Nut		1

56	GB1096-5x40	Flat Key	5x40	1

57	C6266C04701 (m)	Lead Screw		1

58	51103	Thrust Bearing	17x30x9	2

59	C6266C04110-G	Bracket		1

60	GB117-8x30	Taper Pin	8x30	2

61	GB70-M8x20	Hex Socket Cap Screw	M8x20	2

62	GB1155-6	Oil Cup	6	1

63	C6266C04702	Washer		1

64	GB812-M14x1.5	Round Nut	M14x1.5	2

65	C6140W04506	Wipe Plate		1

66	C6266C04727	Gib Setting Screw		1

67	C6250B04728	Cross Slide Gib		1

68	C6250B04102	Cross Slide		1

69	C6250B04701	Sleeve		1

70	GB70-M10x25	Hex Socket Cap Screw	M10x25	2

71	C6140W04714	Cover		1

72	GB818-M5x8	Cross Recessed Pan Head Screw	M5x8	2

73	GB70-M10x55	Hex Socket Cap Screw	M10x55	1

74	GB73-M8x20	Slotted Set Screw	M8x20	1

75	GB119-6x35	Pin	6x35	1

76	C6256C04703-G	Splash Guard		1

79	GB65-M6x30	Slotted Socket Cap Screw	M6x30	2

80	C6266C04727	Gib Adjusting Screw		2

81	GB97.2-5	Washer	5	7

82	C6266C04502A	Liner		1

83	C6266C04729A-G	Cover Plate		1

84	C6266CCA84	Turcite-B (not shown)	620x50x0.8	1

85	C6266CCA85	Turcite-B (not shown)	620x30x0.8	2

86	51104	Bearing (serial #1204ZH0543 and higher)		2

87	C6140W18501	Bracket		1

88	C6266C18502	Gasket		1

92	C613618302	Electrical Warning Label		1

93	51104	Thrust Bearing		2

94	Q81-1-1.4x13x48	Spring (serial #1701ZH0833 and higher)	1.4x13x48	1

95	C6266C04755T-G	Sleeve (serial #1701ZH0833 and higher)		1

96	GB119-3x16	Pin (serial #1701ZH0833 and higher)	3x16	1

Tool Post Assembly　II

Tool Post Assembly　II

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6250B04103	Revolving Plate		1

2	GB6170-M12	Hex Nut	M12	4

3	C6250B04702	Compound Screw		4

4	C6266C04707	Shaft		1

5	C6140W04737	Handle (serial #0809ZH0351 and lower)		1

C6266C04758J-G	Handle (serial #0811ZH0352 and higher)		1

6	GB891-B25	Shaft End Ring (serial #0811ZH0352 and higher)	B25	1

7 	GB117-5x30	Taper Pin (serial #0809ZH0351 and lower)	5x30	1

GB819-M5 x 12	Cross Recessed Head Screw (serial #0811ZH0352 and higher)

M5x12	1

8	C6140W04737	Handle (serial #0809ZH0351 and lower)		1

C6266C04757J-G	Handle (serial #0811ZH0352 and higher)		1

9	C6140W04110	Dial		1

10	C6140W04739	Spring Leaf		1

11	C6266C04736G (m)	Dial		1

12	51104	Thrust Bearing	20x35x10	2

13	GB117-4x25	Taper Pin	4x25	2

14	GB70-M5x14	Hex Socket Cap Screw	M5x14	3

15	C6140W04111	Bearing		1

16	GB1099-5x7.5x19	Half Circle Key	5x7.5x19	1

17 	C6140W04741 (m)	Lead Screw (serial #0809ZH0351 and lower)		1

C6266C04734J	Lead Screw (serial #0811ZH0352 and higher)		1

18	C6266C04301Y (m)	Nut		1

19	GB77-M12x70	Hexagon Socket Set Screws	M12x70	1

21	GB1155-10	Oil Cup	10	2

22	C6250B04104	Longitudinal Slide		1

23	GB1155-6	Oil Cup	6	1

24	C6266C04717	Slide Gib		1

25	C6266C04716	Adjust Screw		1

26	GB73- M10x20	Slotted Set Screw	M10x20	2

27	C6140W04727	Washer		4

28	C6140W04728	Positioning Sleeve		4

29 	C6266C04708	Tool Post (serial #0809ZH0351 and lower)		1

C6266C04708J	Tool Post (serial #0811ZH0352 and higher)		1

30	GB83-M16x50	Square Cap Bolt	M16x50	12

31	C6266C04715	Positioning Pin		1

32	Q81-1-1.6x8x98	Spring	1.6x8x98	2

33	C6266C04712	Spline		1

34	C6266C04709	Flange Disc		1

35	C6140W04732	Bolt		1

36	GB70-M8x16	Hex Socket Cap Screw	M8x16	2

37	C6266C04710	Adjust Washer		1

38	Q81-1-3x32x55	Spring	3x32x55	1

39	C6266C04711-G	Handle		1

40	GB119-5n6x32	Pin	5n6x32	1

41	C6266C04106-G	Lever Support		1

42	GB117-4x40	Taper Pin	4x40	1

Tool Post Assembly　II

#### Index	Part

#### No.	No.	Description	Size	Qty.

43	GB73-M12x14	Slotted Set Screw	M12x14	1

44	GB308-19	Ball	19	1

45	C6266C04713	Connector		1

46	C6266C04714	Connector		1

47	C6140W04738	Lever (serial #0809ZH0351 and lower)		1

C6266C04752JA-G	Handle Seat (serial #0811ZH0352 and higher)		1

48 	GB812-M18x1.5	Round Nut (serial #0809ZH0351 and lower)	M18x1.5	1

GB68-M3×6	Slotted Head Screw (serial #0811ZH0352 and higher)	M3×6	1

49 	GB812-M18x1.5	Round Nut (serial #0809ZH0351 and lower)	M18x1.5	1

C6266C04758J	Locking Nut (serial #0811ZH0352 and higher)		1

50	GB1096-5×12	Flat Key (serial #0811ZH0352 and higher)	5×12	1

51	GB97.2-12	Washer	12	4

### Gear Box Assembly I

Gear Box Assembly I

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6140W05129-G	Upper Cover		1

2	GB70-M6x40	Hex Socket Cap Screw	M6x40	2

3	GB818-M8x12	Cross Recessed Pan Head Screws	M8x12	9

4	C6140W05A729-G	Back Cover		1

6	C6140W05A101-G	Feed Box Casting		1

7	C6140W05766-G	Casting		1

8	C6140W05765-G	Side Splash Guard		1

9	GB818-M3x6	Screw (serial #1601ZH0793 and lower)	M3x6	10

GB2672-M3x6	Screw (serial #1601ZH0794 and higher)	M3x6	10

10	C6140W05A728	Bolt With Washer		3

11	G38-2A-M12x1.25	Bolt	M12x1.25	1

12	G52-1-12	Washer	12	1

13	GB118-10x60	Taper Pin	10x60	2

14	GB70-M12x40	Hex Socket Cap Screw	M12x40	2

15	C6140W05303	Panel (serial #1608ZH0809 and lower)		1

C6250B05303-5	Panel (serial #1608ZH0810 and higher)		1

16	G38-4-M16x1.5	Plug	M16x1.5	1

17	C6140W05770	Oil Pipe		1

18	C6140W05503	Rubber Mat		1

19	C6266C05502	Gasket		1

20	C6140W05773	Cover		1

21	C6266C05502	Gasket		1

22	C6266C05768	Cover		1

23	C6140W05772	Cover		1

24	C6140W05501	Gasket		1

25	GB818-M6x12	Cross Recessed Pan Head Screw	M6x12	12

26	C6140W05726-G	Button Bracket		1

27	GB70-M6x12	Hex Socket Cap Screw	M6x12	2

28 	C6250B18301	Operation Face Plate (serial #1608ZH0809 and lower)		1

C6250B18301-1	Operation Face Plate (serial #1608ZH0810 and higher)		1

Gear Box Assembly　II

## Gear Box Assembly　II

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6140W05109	Sliding Block		7

2	C6140W05A701	Shaft		2

3	C6140W05105	Ratio Change Rocker		1

4	C6140W05709	Rocker Shaft		2

5	GB119-5x14	Pin	5x14	5

6	C6140W05720	Roller		6

7	C6140W05708	Cam		1

8	C6140W05A703	Roller Shaft		1

9	C6140W05702	Shaft		1

10	C6140W05103	Rocker		1

11	C6140W05A710	Shaft		1

12	GB1099-5x19	Key	5x19	6

13	C6140W05707	Shaft		1

14	C6140W05A711	Shaft		2

15	GB119-6x14	Pin	6x14	2

16	C6140W05110	Shaft		1

17	C6140W05106	Upper Rocker		1

18	C6140W05712	Shaft		2

19	GB894.1-16	C-clip For Shaft	16	1

20	C6140W05A717	Cam		2

21	GB308-5	Steel Ball	5	6

22	C6140W05A719	Pulley		2

23	GB73-M6x8	Set Screw	M6x8	2

24	Q81-1-0.6x4x20	Spring 	0.6x4x20	4

25	C6140W05A718	Positioning Column		1

27	G51-2A-25x2.4	Ring Seal	25x2.4	2

27a	G51-2A-16x2.4	Ring Seal	16x2.4	1

28	C6140W05A716	Handle Axle		1

30	C6140W05112	Rocker		1

32	C6140W05A722	Shaft		1

33	C6140W05111	Rocker		1

34	C6140W05A725	Cam		1

35	C6140W05A723	Shaft		1

36	C6140W05A501	Washer		1

37	C6140W05A115-G	Front Cover		1

38	GB70-M10x30	Hex Socket Cap Screw	M10x30	6

39	GB118-8x50	Pin	8x50	2

40	C6266CGBA40	Oil Sight Glass	M27x1.5	1

41	C6140W05721	Shaft		1

42	C6140W05727	Hex Socket Cap Screw		1

43	C6140W05301-6	Panel (serial #1608ZH0809 and lower)		1

C6250B05301-11	Panel (serial #1608ZH0810 and higher)		1

45	C6140W05A704	Positioning Disc		1

46	GB68-M5x12	Recessed Sunk Head Screw	M5x12	6

47	C6140W05A104-G	Lever Support		1

48	C6140W05705-G	Lever		2

49	GB308-10	Steel Ball	10	3

## Gear Box Assembly　II

#### Index	Part

#### No.	No.	Description	Size	Qty.

50	Q81-1-1x8x25	Spring	1x8x25	3

51	GB73-M12x14	Slotted Set Screws	M12x14	3

52	C6140W05706-G	Disk		2

53	GB819-M5x12	Cross Recessed Head Screws	M5x12	3

54	C6140W05A108	Sleeve		1

55	C6140W05A713	Positioning Disc		1

56	C6140W05A107-G	Lever Support		1

57	C6266C05714-G	Lever		1

58	C6140W05715-G	Cover		1

59	C6140W05A724	Positioning Disc		1

60	C6140W05A104-G	Lever Support		1

61	C6140W05308	Handle Panel (serial #1608ZH0809 and lower)		1

C6140W05308-3	Handle Panel (serial #1608ZH0810 and higher)		1

62	C6140W05A307	Handle Panel (serial #1608ZH0809 and lower)		1

C6140W05A307-2	Handle Panel (serial #1608ZH0810 and higher)		1

63	C6140W05306	Handle Panel (serial #1608ZH0809 and lower)		1

C6140W05306-2	Handle Panel (serial #1608ZH0810 and higher)		1

64	GB818-M3x6	Cross Recessed Pan Head Screw (serial #1601ZH0793 and lower)

M3x6	21

GB2672-M3x6	Screw (serial #1601ZH0794 and higher)	M3x6	21

65	GH-2040ZHK974	Label (For GH-2040ZH only)		1

GH-2060ZHK975	Label (For GH-2060ZH only)		1

GH-2080ZHK976	Label (For GH-2080ZH only)		1

Gear Box Assembly　III

Gear Box Assembly　III

#### Index	Part

#### No.	No.	Description	Size	Qty.

3	C6140W05A730	I Shaft		1

4	C6140W05A116	Bearing Cover (serial #0808ZH0339 and lower)		1

C6266C05772J	Bearing Cover (serial #0809ZH0340 and higher)		1

5 	G51-1-35	Oil Seal (serial #0808ZH0339 and lower)…..	35	2

G51-1-B-35x50x8	Oil Seal (serial #0809ZH0340 and higher)	B-35x50x8	2

6	6305	Bearing	25x62x17	1

7	GB894.1-25	C-clip For Shaft	25	3

8	C6140W05731	Double Gear		1

9	6203	Bearing	17x40x12	9

10	C6140W05732	Gear		1

11	6205	Bearing	25x52x15	1

12	C6140W05A769	Washer		5

13	C6140W05733	Double Gear		2

14	6005	Bearing	25x47x12	5

15	C6140W05736	Sleeve		1

16	GB1099-4x19	Key	4x19	1

17	C6140W05A735	V Shaft		1

18	C6140W05A738	VII Shaft		1

19	C6140W05737	Triple Gear		1

20	C6140W05739	Gear		1

21	C6140W05743	VIII Shaft		1

22	16006	Bearing	30x55x9	2

23	C6140W05740	Sleeve		2

24	51106	Bearing	30x47x11	2

25	C6140W05117-G	Flange Sleeve		1

25a	C6140W05A503	Gasket		1

26	GB70-M10x25	Hex Socket Cap Screw	M10x25	8

28	C6140W05A118	Sleeve (serial #0808ZH0339 and lower)		1

C6266C05773J	Sleeve (serial #0809ZH0340 and higher)		1

29 	C6140W05A741	Bearing Cover (serial #0808ZH0339 and lower)		1

C6266C05741J	Bearing Cover (serial #0809ZH0340 and higher)		1

30	C6140W05742	Round Nut		2

31	C6140W05767	Shaft		1

32	GB117-6x40	Taper Pin	6x40	4

33	G38-4A-M16x1.5	Plug	M16x1.5	2

34	C6140W05A771	Bearing Cover		1

35	6303	Bearing	17x47x14	1

36	C6140W05A762	II Shaft		1

37	C6140W05763	Gear		1

38	C6140W05764	Gear		1

39	C6140W05125	Sleeve		1

40	C6140W05751	Sleeve		2

41	C6140W05A752	Adjust Washer		2

42	C6140W05A754	IV Shaft		1

43	C6140W05A759	Gear		1

44	C6140W05758	Gear		1

45	C6140W05757	Gear		1

Gear Box Assembly　III

#### Index	Part

#### No.	No.	Description	Size	Qty.

46	C6140W05A734	Positioning Sleeve		2

47	GB75-M8x10	Slotted Set Screws 	M8x10	2

48	C6140W05756	Gear		1

49	C6140W05755	Gear		1

50	C6140W05753	Gear		1

51	C6140W05A749	Shaft (Ⅵ)		1

52	C6140W05750	Gear		1

53	C6140W05A748	Gear		1

54	C6140W05A124	Sleeve		1

55	C6140W05747	Gear		1

56	C6140W05746	Gear		1

57	C6140W05745	IX Shaft		1

58	C6140W05A744	Sleeve		1

59 	C6140W05A121	Flange Sleeve (serial #0808ZH0339 and lower)		1

C6266C05121W	Flange Sleeve (serial #1601ZH0793 and lower)		1

C6140W05A121-G	Flange Sleeve (serial #1601ZH0794 and higher)		1

59a	C6140W05A504	Gasket		1

60	G51-1-25	Oil Seal (serial #0808ZH0339 and lower)	25	1

G51-1-B-25x40x7	Oil Seal (serial #0809ZH0340 and higher)..	B-25x40x7	1

61	C6140W05768	Shaft Connector		1

62	C6140W05A770	Bearing Cover		1

63	6304	Bearing	20x52x15	1

64	C6140W05761	Double Gear		1

66	C6140W05A760	III Shaft (serial #0808ZH0339 and lower)		1

C6266C05760W	III Shaft (serial #1601ZH0793 and lower)		1

C6140W05A760	III Shaft (serial #1601ZH0794 and higher)		1

67 	GB894.1-17	C-clip For Shaft (serial #0808ZH0339 and lower	17	1

GB879-6x25	Straight Pin (serial #0809ZH0340 and higher)	6x25	1

68 	C6140W05A123	Sleeve (serial #0808ZH0339 and lower)		.1

C6266C05770W	Shaft (serial #1601ZH0793 and lower)		.1

C6140W05A772	Shaft (serial #1601ZH0794 and higher)		.1

69	C6140W05122	Sleeve		1

70	C6266C05130J	Oil Splash Ring (serial #0809ZH0340 and higher)		2

71	GB78-M6×12	Slotted Set Screw (serial #0809ZH0340 and higher)	M6×12	2

72	6002……………………..Bearing (serial #0809ZH0340 and higher)	15×32×9	1

73	C6266C05774J	Sleeve (serial #0809ZH0340 and higher)		1

74	C6266C05123J	Sleeve (serial #0809ZH0340 and higher)		1

75	GB77-M6×12	Slotted Set Screw (serial #0809ZH0340 and higher)	M6×12	2

Apron Assembly　I

Apron Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6266C06101-G	Apron Casting		1

2	GB71-M8x10	Set Screw	M8x10	2

3	C6266C06506	Gasket		1

4	C6140W06750	Back Cover		1

5	GB819-M8x16	Cross Recessed Countersunk Head Screw	M8x16	8

6	GB3452.1-8.75x1.8G	Ring Seal	8.75x1.8G	1

7	GB68-M6x10	Recessed Sunk Head Screw	M6x10	4

8	C6140W06731	Cover		1

9	GB71-M6x10	Slotted Set Screw	M6x10	1

10	GB878-10x35	Parallel Pins With External Thread	10x35	1

11	GB1096-6x14	Pin	6x14	1

12	C6140W06715	Block		1

20	C6140W06302Y	Half Nut (For Metric style)		1

21	C6140W06107	Lower Nut		1

22	C6140W06108	Upper Nut		1

23	C6140W06759	Gib		1

24	GB6170-M10	Hex Nut	M10	2

25	C6140W06758	Cylindrical End Set Screw		1

26	GB119-12x25	Pin	12x25	2

27	GB73-M10x25	Slotted Set Screw	M10x25	1

28	GB894.1-30	C-clip For Shaft	30	1

29	C6140W06755	Collar		1

30	C6266C06105-G	Positioning Block		1

31	GB117-6x35	Taper Pin	6x35	1

32	C6266C06106-G	Lever Support		1

33	GB70-M6x16	Hex Socket Cap Screw	M6x16	2

34	Q81-1-1.2x8x22	Spring	1.2x8x22	1

35	GB119-8x14	Pin	8x14	1

36a	GB79-M8x20	Hex Socket Set Screws	M8x20	2

36b	GB6172-M8	Hex Nut	M8	2

37	C6266C06711-G	Control Handle (serial # 0803ZH0086 and lower)		1

C6266C06711J-G	Control Handle (serial # 0803ZH0087 and higher)		1

38	GB117-5x30	Taper Pin	5x30	1

39	C6266C06710	Positioning Sleeve		1

40	GB308-10	Steel Ball	10	1

41	Q81-1-1.5x8x35	Spring	1.5x8x35	1

42	GB73-m12x14	Slotted Set Screw	m12x14	1

43	C6266C06A780	Positioning Sleeve		1

44	C6140W06716	Bolt		1

45	C6140W06725	VII Shaft		1

46	C6140W06303Y	Sleeve		1

47	GB119-5x60	Pin	5x60	1

48	C6140W02801-G	Handle		1

49 	C6266C06104	Sleeve		1

50	R51-2-20	Oil Sight Glass	20	1

51	C6140W06760-G	Front Cover		1

52	GB65-M6x10	Slotted Socket Cap Screw	M6x10	4

Apron Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

53	C6266C06713	Pump Cover		1

54	C6266C06505	Gasket		1

55	C6266C06504	Gasket		1

56	Y91-1A-8	Nut	8	1

57	C6266C06727	Sleeve		1

58	T3-M-Ø6x0.75x450	Copper Pipe	Ø6x0.75x450	1

59	C6266C06726	Valve		1

60	C6266C06714	Adjust Bolt		2

61	Q81-1-0.3x3x12	Spring	0.3x3x12	2

62	GB308-5	Steel Ball	5	4

63	C6266C06715	Oil Purifier		1

64	C6266C06107-G	Pump		1

65	GB65-M6x12	Slotted Socket Cap Screw	M6x12	3

66	G51-2A-20x2.4	Ring Seal	20x2.4	1

67	C6266C06712	Piston-rod (serial # 0803ZH0086 and lower)		1

C6266C06712J	Piston-rod (serial # 0803ZH0087 and higher)		1

68	Q81-1-1.2x19x70	Spring	1.2x19x70	1

69	GB4141.11-M8x25	Ball (serial # 0803ZH0086 and lower)	M8x25	1

1440R04783-G	Knob (serial # 0803ZH0087 and higher)		1

70	C6266C06502	Gasket		1

71	C6266C06103-G	Bottom Cover		1

72	GB70-M8x12	Hex Socket Cap Screw	M8x12	6

73	GB38-2-M12x1.5	Drain Plug	M12x1.5	1

74	C6266C06725	Shaft		1

75	C6266C06109	Rocker		1

76	C6266C06724	Collar		1

77	GB894.1-15	C-clip For Shaft	15	1

78	C6266C06721	Rod		1

79	G51-2A-12x1.9	Ring Seal	12x1.9	1

80	C6266C06723	Sleeve		1

81	C6266C06722	Block		1

82	606	Bearing	6x17x6	1

83	GB119-5n6x15	Pin	5n6x15	1

84	GB70-M6x25	Hex Socket Cap Screw	M6x25	2

85	GB119-8n6x45	Pin	8n6x45	1

86	C6266C06110	Positioning Block		1

87	C6140W06116A-G	Bracket Disk (For Metric style)		1

88	GB119-6x25	Pin	6x25	1

89	C6140W06761	Dial (For Metric style)		1

90	C6140W06769	Spring Leaf		1

91	GB119-8h8x50	Pin	8h8x50	1

92	C6140W06768	Eccentric Shaft (serial # 0804ZH0125 and lower)		1

C628006730-G	Eccentric Shaft (serial # 0805ZH0126 and higher)		1

93	GB119-3n6x22	Pin (serial # 0804ZH0125 and lower)	3n6x22	1

Q81-1-0.4x3x10	Spring (serial # 0805ZH0126 and higher)	0.4x3x10	1

94	C6140W06762	Gear (For Metric style)		1

95	C6140W06117	Bracket (For Metric style)		1

Apron Assembly　I

#### Index	Part

#### No.	No.	Description	Size	Qty.

96	GB70-M8x55	Hex Socket Cap Screw	M8x55	3

97	GB119-12n6x40	Pin	12n6x40	2

98	C6266C06501	Gasket		1

99	GB117-4x18	Taper Pin	4x18	1

100	GB68-M6x12	Recessed Sunk Head Screw	M6x12	4

101	C6140W06109-G	Handle Seat		1

102	C6266C06740J	Wire Baffle (serial #1301ZH0609 and higher)		1

104	GB70-5x25	Hex Socket Cap Screw (serial #1301ZH0609 and higher)	5x25	2

105	GB75-5x16	Slotted Cylindrical End Set Screw	5x16	1

106	C6266C06702-G	Level Sleeve		1

108	C6266C06303	Label (serial #1608ZH0809 and lower)		1

C6266C06303-10	Label (serial #1608ZH0810 and higher)		1

109 	GB818-M3x6	Cross Recessed Pan Head Screw (serial #1601ZH0793 and lower)

M3x6	4

GB2672-M3x6	Screw (serial #1601ZH0794 and higher)	M3x6	4

110	C6266C06305	Label (serial #1608ZH0809 and lower)		1

C6266C06305-1	Label (serial #1608ZH0810 and higher)		1

Apron Assembly　II

Apron Assembly　II

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6140W06738	Adjust Knob		1

2	GB6172-M12	Hex Flat Nut	M12	1

3	GB78-M12x60	Hex Set Screw (serial #1307ZH0671 and lower)	M12x60	1

C6266C06779	Screw (serial #1309ZH0672 and higher)		1

4	GB70-M8x20	Hex Socket Cap Screw	M8x20	3

5	C6140W06111	Flange (serial #1307ZH0671 and lower)		1

C6266C06111A-G	Flange (serial #1309ZH0672 and higher)		1

6	G51-2A-93x3.1	Ring Seal	93x3.1	1

7	GB70.3-M5x12	Screw	M5x12	1

8	C6140W06739	Adjust C-clip		1

9	30502/P6	Bearing	25x52x15	2

10	C6266C06730	Bolt		4

11	C6140W06740	Washer		1

12	Q81-1-1x10x35	Spring (serial #1307ZH0671 and lower)	1x10x35	4

Q81-1-1.2x10x35	Spring (serial #1309ZH0672 and higher)	1.2x10x35	4

13	C6266C06707	Clutch		1

14	GB894.1-30	C-clip For Shaft	30	1

15	C6266C06708	Washer		1

16	C6266C06706	Clutch		1

17	GB1096-8x16	Flat Key	8x16	1

18	C6140W06708	Star Gear		1

19	C6140W06709	Gear		1

20	C6140W06726	Pin		3

21	C6140W06710	Washer		1

22	C6140W06737	Block		1

23	GB67-M6x10	Slotted Pan Head Screw	M6x10	1

24	C6140W06729	Splash Leaf		1

25	C6266C06209	Worm (serial #1307ZH0671 and lower)		1

C6266C06209A	Worm (serial #1309ZH0672 and higher)		1

26	C6140W06728	Motor Connector		1

27	C6266C06503	Washer		1

28	GB1096-4x14	Flat Key	4x14	1

29	YSS56BJ-G	Motor	370W 1400r/min	1

30	GB5782-M8x30	Hexagon Head Bolt	M8x30	3

31	C6140W06736	IX Shaft		1

32	C6140W06735	Washer		2

33	C6140W06734	Gear		1

34	C6140W06306	Sleeve		1

35	GB894.1-16	C-clip For Shaft	16	1

36	C6140W06305	Sleeve		1

37	C6140W06733	X Shaft		1

38	GB1096-6x25	Flat Key	6x25	1

39	C6140W06732	Gear		1

40	C6140W06304	Sleeve		1

41	C6140W06730	Washer		1

42	GB894.1-38	C-clip For Shaft	38	1

43	C6266C6704A	Oil Tap Cover		1

Apron Assembly　II

#### Index	Part

#### No.	No.	Description	Size	Qty.

44	C6266C06705A-35	Oil Tap	35	1

45	C6266C04A311	Label (serial #1608ZH0809 and lower)		1

C6266C04A311-1	Label (serial #1608ZH0810 and higher)		1

46	C6266C06102	Plug		1

47	C6140W06103	Fork		1

49	C6266C06701	Control Shaft		1

50	GB67-M6x8	Slotted Pan Head Screw	M6x8	3

52	Q81-1-1.6x8x22	Spring	1.6x8x22	3

51	C6140W06701	Pin		3

53	C6140W06713	Left Fork		1

54	GB119-6n6x14	Pin	6n6x14	6

55	C6140W06715	Sliding Block		6

56	C6140W06714	Right Fork		1

57	C6140W06717	Shaft		1

58	C6140W06104	Inter-locking Block		1

59	GB117-5x30	Taper Pin	5x30	1

60	C6140W06718	Shaft		1

61	C6266C06304	Sleeve		1

62	GB70-8x20	Hex Socket Cap Screw	8x20	5

63	C6140W06719	Bracket		1

64	C6140W06105-G	Bracket		1

65	GB71-M6x10	Slotted Set Screw	M6x10	1

66	C6140W06722A-G	Handle		1

67	C6140W06106-G	Cross Cover		1

68	C6140W06501	Washer		1

70	C6140W06721A-G	Handle		1

71	C6140W06720A-G	Seat		1

72	C6140W06727	Pin		3

73	Q81-1-0.3x3x12	Spring	0.3x3x12	3

74	GB1099-5x19	Half Circle Key	5x19	1

75	C6140W06704	XIII Shaft		1

76	C6140W06705	Collar		1

77	GB894.1-14	C-clip For Shaft	14	1

78	GB71-M5x6	Slotted Set Screw	M5x6	1

Apron Assembly　III

## Apron Assembly　III

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6140W06751	Gear		1

2	GB71-M6x8	Slotted Set Screw	M6x8	2

3	C6140W06309	Sleeve		1

4	C6140W06752	Gear		1

5	C6266C06728	VI Shaft		1

6	C6140W06754	Washer		1

7	GB894.1-20	C-clip For Shaft	20	2

8	C6140W06114	Plug		1

9	C6140W06113	Sleeve		3

10	C6140W06749	Gear		1

11	C6140W06308	Worm Wheel		1

12	GB72-M8x16	Slotted Set Screw	M8x16	1

13	GB1099-6x22	Half Circle Key	6x22	1

14	GB1099-8x28	Half Circle Key	8x28	1

15	C6140W06748	IV Shaft		1

16	C6140W06115	Sleeve		3

17	G51-2A-35x3.1	Ring Seal	35x3.1	3

18	C6140W06746	Gear		2

19	C6140W06307	Sleeve		4

20	GB71-M6x10	Slotted Set Screw	M6x10	4

21	C6140W06744	Gear		4

22	GB1099-5x16	Half Circle Key	5x16	2

23	C6140W06747	III Shaft		2

24	C6140W06745	Connector		2

25	C6140W06743	II Shaft		1

26	GB1099-8x28	Half Circle Key	8x28	1

27	G51-2A-32x3.5	Ring Seal	32x3.5	1

28	C6140W06742	Gear		1

29	C6140W06118	Sleeve		1

30	C6140W06764	Gear		1

31	GB117-5x35	Taper Pin (serial #1209ZH0608 and lower)	5x35	1

GB877-5x40	Taper Pin (serial #1301ZH0609 and higher)	5x40	1

32	C6140W06112	Plug		1

33	C6140W06774	Washer		1

34	Q81-1-1.6x18x25	Spring	1.6x18x25	1

35	C6140W06773	Connector		1

36	C6140W06772	Washer		1

37	C6140W06311	Sleeve		1

38	C6140W06771	Gear		1

39	C6140W06770	Washer		1

40	C6140W06120	Sleeve		1

41	G51-2A-18x2.4	Ring Seal	18x2.4	1

42	C6140W06775	I Shaft		1

43	GB91-4x25	Pin	4x25	1

44	GB1096-4x20	Flat Key	4x20	1

45	GB1099-5x16	Half Circle Key	5x16	1

46	C6266C06111-G	Handle Wheel		1

## Apron Assembly　III

#### Index	Part

#### No.	No.	Description	Size	Qty.

47	GB895-10	Steel C-clip	10	1

48	C6140W06766-G	Shaft		1

49	C6140W06765-G	Lever Sleeve		1

50	GB891-B25	Circlip	B25	1

51	GB68-M5x12	Recessed Sunk Head Screw	M5x12	1

52	C6140W06763	Gear		1

53	C6140W06310Y	Sleeve		1

54 	GB119-12n6x40	Pin	12n6x40	1

56	G51-2A-25x2.4	O Ring Seal	25x2.4	1

## Apron Assembly　Ⅳ

## Apron Assembly　Ⅳ

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	GB1155-10	Oil Cup	10	1

2	C6266C11703	Handle		1

3	C6266C11301 (m)	Label (serial #1608ZH0809 and lower)		1

C6266C11301-1(m)	Label (serial #1608ZH0810 and higher)		1

4	C6266C11702	Shaft		1

5	GB1096-4×15	Flat Key	4×15	1

6	GB818- M4×8	Cross Recessed Pan Head Screw	M4×8	7

7	C6266C11701	Cover		1

8	GB5782- M12×110	Hex Cap Bolt	M12×110	1

8a	GB93-12	Spring Washer	12	1

9	GB97.2-12	Flat Washer	12	1

10	C6266C11101-G	Casting		1

11	C6266C11705	Sleeve		1

12	GB827-2×5	Aluminium Rivet	2×5	4

13 	C6266C11302 (m)	Label (serial #1608ZH0809 and lower)		1

C6266C11302-1(m)	Label (serial #1608ZH0810 and higher)		1

14	C6266C11704	Cover Casting		1

15	C6266C11102	Helical Gear		1

C6266C11103	Helical Gear (For Attachment)	m3.75z14	1

16	C6266C11706	Washer		1

17	GB70- M5×10	Hex Socket Cap Screw	M5×10	1

### Gear Assembly

## Gear Assembly

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6250B08701-G	Splash Guard		1

2	GB818-M6x8	Cross Recessed Pan Head Screws (serial #1601ZH0793 and lower)

M6x8	2

GB2672-M6x8	Screw (serial #1601ZH0794 and higher)	M6x8	2

3	C6250B08702 (m)	Gear	2.5m60T	1

4	GB6172-M20	Nut	M20	1

5	GB97.2-20	Washer	20	1

6	C6250B08101	Gear Frame		1

7	C6140W02824	Fixing Rod-2		1

8	C6140W08703	Nut Cover		1

9	C6140W08702	Gear Shaft		1

10	C6140W08301	Spline Sleeve		1

11	C6250B08102 (m)	Gear	2.5m69T	1

12	C6140W08701	Washer		1

13	GB119-8n6x20	Pin	8n6x20	1

14	C6140W08704	Position Nut		1

15	C6250B08703 (m)	Gear	2.5m56T	1

16	C6250B08704 (m)	Gear	2.5m57T	1

17	1440R06001C-2	Collar (The sum is adopt to the space between 15 and 16)	not sure

18	GB5782-M12x30	Hexagon Head Bolt	M12x30	1

19	GB851-A12-40	Snap Washer	A12-40	2

20	GB5783-M12x20	Hexagon Head Bolts	M12x20	1

Micro Carriage Stop Assembly

Micro Carriage Stop Assembly

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6266C26102-G	Left Support		1

2	GB1155-8	Oil Cup	8	2

3	GB70-M10x40	Hex Socket Cap Screw	M10x40	4

3a	GB97.2-10	Washer	10	4

4	GB118-8x40	Pin	8x40	4

5	C6266C26712	Eccentric Travel Setting Ring		6

6	GB77-M8x8	Hex Socket Set Screws	M8x8	12

7	GB119-4x10	Set Screw	4x10	6

8	C6266C26713	Locking Key		6

9	C6266C26706	Shaft Connector		1

10	GB117-6x35	Taper Pin	6x35	1

11	C6266C26101-G	Right Support		1

12	GB308-8	Steel Ball	8	1

13	GB2089-1.5x8 x20	Spring	1.5x8 x20	1

14	GB77-M10x40	Hex Socket Set Screws	M10x40	1

15	C6266C26701	Sleeve		1

16	GB812-M39x1.5	Round Nut	M39x1.5	2

17	C6266C26702	Sleeve		1

18	C6266C26301	Label		1

19	GB867-M3×8	Half Circle Rivet	M3×8	5

19a	C6136ZK03303B	Label		1

20	C6266C26714	Sleeve		1

21	GB79-M6×8	Hex Socket Set Screws	M6×8	1

22	C6266C26704	Shaft		1

23	GB2089-1.2×13×40	Spring	1.2×13×40	1

24	C6266C26703	Sleeve		1

25	C6266C26707A	Travel Setting Rod (For GH-2040ZH only)		1

C6266C26707B	Travel Setting Rod (For GH-2060ZH only)		1

C6266C26707C	Travel Setting Rod (For GH-2080ZH only)		1

C6266C26707D	Travel Setting Rod (For GH-20120ZH only)		1

26	C6266C26705	Handle		1

27	GB117-4x25	Taper Pin	4x25	1

28	GB75-M4×6	Slotted Socket Cap Screw	M4×6	1

29	GB71-M4×8	Slotted Set Screw	M4×8	1

Brake Assembly

## Brake Assembly

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6266C22705	Braking Belt		1

2	GB70-M6x8	Hex Socket Cap Screw	M6x8	4

5	C6266C22704	Bolt		1

6	GB6170-M12	Hex Nut	M12	2

7	C6266C22103-G	Braking Belt Support		1

8	GB70-M8x20	Hex Socket Cap Screw	M8x20	3

9	C6266C22706	Brake Block		1

10	C6266C22104-G	Fork		1

11	GB70-M8x20	Hex Socket Cap Screw	M8x20	1

12	GB91-3x20	Screw	3x20	1

13	C6266C22707	Pin Shaft		1

14	GB879-5x35	Spring Pin	5x35	1

15	C6266C22101-G	Support (For GH-2040ZH, GH-2060ZH, GH-2080ZH)		2

C6266C22101-G	Support (For GH-20120ZH only)		4

17	C6266C22102-G	Brake Support (For GH-2040ZH, GH-2060ZH, GH-2080ZH)	2

C6266C22102-G	Brake Support (For GH-20120ZH only)		4

18	GB77-M8x8	Hex Socket Set Screws (For GH-2040ZH, GH-2060ZH, GH-2080ZH)

M8x8	2

GB77-M8x8	Hex Socket Set Screws (For GH-20120ZH only)	M8x8	4

19	Q81-1-2.5x18x80	Spring (For GH-2040ZH, GH-2060ZH, GH-2080ZH)	2.5x18x80	2

Q81-1-2.5x18x80	Spring (For GH-20120ZH only)	2.5x18 x80	4

20	C6266C22702	Screw (For GH-2040ZH, GH-2060ZH, GH-2080ZH)		2

C6266C22702	Screw (For GH-20120ZH only)		4

21	C6266C22105-G	Brake Support (For GH-2040ZH only)		2

C6266C22105-G	Brake Support (For GH-2060ZH, GH-2080ZH)		3

C6266C22105-G	Brake Support (For GH-20120ZH only)		6

22	GB70-M10x35	Hex Socket Cap Screw (For GH-2040ZH only)	M10x35	2

GB70-M10x35	Hex Socket Cap Screw (For GH-2060ZH, GH-2080ZH)	M10x35	3

GB70-M10x35	Hex Socket Cap Screw (For GH-20120ZH only)	M10x35	6

23	GB879-6x45	Spring Pin (For GH-2040ZH only)	6x45	2

GB879-6x45	Spring Pin (For GH-2060ZH, GH-2080ZH)	6x45	3

GB879-6x45	Spring Pin (For GH-20120ZH only)	6x45	6

24 	GB70-M6x20	Hex Socket Cap Screw (For GH-2040ZH only)	M6x20	4

GB70-M6x20	Hex Socket Cap Screw (For GH-2060ZH, GH-2080ZH)	M6x20	6

GB70-M6x20	Hex Socket Cap Screw (For GH-20120ZH only)	M6x20	12

25	C6266C22708A-G	Pedal (For GH-2040ZH only)		1

C6266C22708B-G	Pedal (For GH-2060ZH only)		1

C6266C22708C-G	Pedal (For GH-2080ZH only)		1

C6266C22708D-G	Pedal (For GH-20120ZH only)		2

26	C6266C22703A-G	Shaft (For GH-2040ZH only)		1

C6266C22703B-G	Shaft (For GH-2060ZH only)		1

C6266C22703C-G	Shaft (For GH-2080ZH only)		1

C6266C22703D-G	Shaft (For GH-20120ZH only)		1

27	GB819-M5x12	Cross Recessed Countersunk Head Screw	M5x12	4

27a	GB6172-M5	Hex Nut	M5	4

28	GB70-M8x20	Hex Socket Cap Screw (For GH-2040ZH, GH-2060ZH, GH-2080ZH)

M8x20	12

## Brake Assembly

#### Index	Part

#### No.	No.	Description	Size	Qty.

GB70-M8x20	Hex Socket Cap Screw (For GH-20120ZH only)	M8x20	20

29	GB78-M8x16	Hex Socket Cap Screw	M8x16	3

30	C6266C22106-G	Support		1

31	C6266C22107-G	Sleeve		1

32	C6266C22701	Screw (For GH-2040ZH, GH-2060ZH, GH-2080ZH)		2

C6266C22701	Screw (For GH-20120ZH only)		4

33	C6266C18705-G	Bracket		1

34	GB70-M6x12	Hex Socket Cap Screw	M6x12	3

35	GB97-6	Washer	6	3

36	ZH-SQ2	Limit Switch	JW2-11H/W1	1

37	GB818-M4x20	Cross Recessed Pan Head Screw	M4x20	2

38	GB6172-M6	Hex Nut	M6	2

##### Steady Rest Assembly

## Steady Rest Assembly

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	GB4141.29-Φ12	A Type Asterisk Handle	Φ12	3

2	C6266C10702	Sliding Sleeve		3

3	GB117-4x25	Pin	4x25	3

4	C6266C10701	Slotted Set Screw		3

5	C6140ZK10B701	Lever (serial #1601ZH0794 and higher)		3

6	6000-2RS	Bearing (serial #1601ZH0794 and higher)	10x26x8	3

6a	C6140ZK10B702	Shaft (serial #1601ZH0794 and higher)		3

7	GB4141.29-M12	B Type Asterisk Handle	M12	1

8	C6250B10A102-G	Steady Rest Upper Body		1

9	C6140W10701	Screw		1

10	GB75-M10x16	Slotted Set Screw	M10x16	3

11	C6140W10704	Set Screw		3

12	GB119-A6x45	Pin	A6x45	3

13	GB119–A16x55	Pin	A16x55	1

14	C6250B10A101-G	Steady Rest Lower Body		1

15	GB119-A8x55	Pin	A8x55	1

16	GB56-M20	Hex Extra Thick Nut	M20	1

17	GB97.2-20	Washer	20	1

18	C6140W10104-G	Clamping Plate		1

19	C6140W10706	Square Head Bolt		1

### Follow Rest Assembly

Follow Rest Assembly

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	GB4141.29-Φ12	A Type Asterisk Handle	Φ12	2

2	C6250B10701	Screw		2

3	GB117-4x25	Pin	4x25	2

4	C6266C10704	Nut		2

5 	C6266C10706	Sliding Sleeve		2

6 	C6266C10302	Block		2

7	C6250B10103-G	Follow Rest Casting		1

8	GB75-M10x14	Slotted Set Screw	M10x14	2

9	GB119-6x45	Pin	6x45	2

10 	C6140W10704	Set Screw		1

11	GB70-M16x55	Hex Socket Cap Screw	M16x55	2

###### Safety Guard Cover

###### Safety Guard Cover

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6250B19701	Protection Guard (serial #1601ZH0793 and lower)		1

C6250B19701A	Protection Guard (serial #1601ZH0794 and higher)		1

2	ZX19501E	Protection Guard Visual Glass		1

3	ZX19704E	Fixing Rod		1

4 	ZXS04E	Handle (serial #1601ZH0793 and lower)	Z96-6	1

A=90 Black	Handle (serial #1601ZH0794 and higher)		1

6	GB70-M6x12	Hex Socket Cap Screw (serial #1601ZH0794 and higher)	M6x12	2

7	ZXS07E	Hexagon Thin Nut	M4	4

8	ZXS08E	Plain Washer	4	4

8a	GB96-4	Large Plain Washer	4	4

9	ZXS09E	Cross Recessed Pan Head Screw	M4x12	4

10	ZXS10E	Plain Washers	5	4

11	ZXS11E	Hexagon Socket Cap Head Screw	M5x16	4

12	ZX19703E	Rest Bar		1

13	ZXS13E	Slotted Set Screw	M8x10	2

14	ZXS14E	Hexagon Socket Cap Head Screw	M6x30	4

15	ZXS15E	Hexagon Socket Set Screw	M8x16	1

16	GH1440A19101E	Switch Box		1

17	SQ4E	Stroke Switch	LXW5-11Q1	1

18	ZXS18E	Slotted Pan Head Screw	M4x25	2

19	ZX19702E	Shaft		1

20	ZX19502E	Gasket		1

21	C6266CCGA21-M12	Nut	M12	1

22	C6250B19702	Board (serial #1601ZH0793 and lower)		1

C6250B19702A	Board (serial #1601ZH0794 and higher)		1

23	GB6172-M6	Hex Nut	M6	2

24	GB97.2-6	Flat Washer	6	2

Parts List for Toolpost Protection Device

Parts List for Toolpost Protection Device

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6266C20501	Shield		1

2	GH1640ZX20701	Clamping Screw		1

3	GH1640ZX20703	Washer		1

4	GH1640ZX20704	Sleeve		1

5	GB6170-M6	Nut	M6	3

6	GH1640ZX20705-1	Bracket		1

7	GB70-M8x16	Hex Socket Cap Screw	M8x16	2

8	GH1640ZX20705-2	Bracket		1

9	GB71-M4x8	Slotted Set Screw 	M4x8	1

10	GB97.2-6	Flat Washer 	6	6

11	GB818-M6x20	Cross Recessed Pan Head Screw 	M6x20	3

Parts List for Lead Screw Protection Device

Parts List for Lead Screw Protection Device

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6140W05765-G	Side Plate		1

2	C6266C07701-1	Connect Sleeve		1

3	GB73-M5x8	Slotted Set Screw With Flat Point	M5x8	1

4	1440R07704	Sleeve		1

5	GB819-M5x12	Cross Recessed Countersunk Head Screw	M5x12	13

6	LGB-45-1000-100	Telescoping Sheet Cover (1000 Size)		2

LGB-45-1500-150	Telescoping Sheet Cover (1500 Size)		2

LGB-45-2000-120	Telescoping Sheet Cover (2000 Size)		2

7	1440R07702A	Flange		1

8	1440R07706A	Sleeve 		1

9	C6266C07702A	Left Support		1

10	GB819-M5x18	Cross Recessed Head Screw 	M5x18	3

11	GB70-M6x16	Hex Socket Cap Screw	M6x16	7

12	C6266C07703	Right Support		1

13	1440R07702A	Flange		1

14	1440R07705A	Right Flange 		1

15	C6266C11708	Cover		1

16	GB819-M5x10	Cross Recessed Countersunk Head Screw	M5x10	4

Parts List for Lead Screw Protection Device

For GH-20120ZH

Parts List for Lead Screw Protection Device

For GH-20120ZH

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	C6266C07705-G	Front Left Support		1

2	GB819-M4x8	Cross Recessed Head Screw 	M4x8	20

3	C6266C07706-G	Front Right Support		1

4	C6266CLSG004	Roll-up Cover	3000	2

5	C6266C07707-G	Back Left Support		1

6	C6266C07708-G	Back Right Support		1

## Coolant & Work Light Assembly

## Coolant & Work Light Assembly

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	AB-25-ID1/2″×1280	Rubber Tube (For GH-2040ZH only)	ID 1/2″×1280	1

AB-25-ID1/2″×1780	Rubber Tube (For GH-2060ZH only)	ID 1/2″×1780	1

AB-25-ID1/2″×2280	Rubber Tube (For GH-2080ZH only)	ID 1/2″×2280	1

AB-25-ID1/2″×3000	Rubber Tube (For GH-20120ZH only)	ID 1/2″×3000	1

2	GB5782-M6×16	Hexagon Head Bolt (For GH-2040/60/80ZH)	M6×16	4

GB70-M6 x16	Hex Socket Cap Screw (For GH-20120ZH only)	M6×16	4

3	GB6172-M6	Hex Nut	M6	4

4	AB-25-1/8HP	Coolant Pump	1/8HP	1

5	GB41-M6	Hex Nut	M6	2

6	C613601727	Clip For Rubber Tube		1

7	GB818-M6×20	Cross Recessed Pen Head Screw	M6×20	2

8	C6140W01731	Fitting		1

9	C6140W01730	Flow Pipe		1

10	AB-25-1/2″×16×700	Coolant Tube	1/2″×16×700	1

11	GB70-M6×20	Hex Socket Cap Screw	M6×20	4

12	JC52	Light (serial #1601ZH0793 and lower)	24V 50W	1

JC52B	Light (serial #1601ZH0794 and higher)	24V 12W	1

13	ZX01510	Coolant Tank		1

14	K989	Label		1

###### Carriage Lubrication

Carriage Lubrication– Parts List

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	GB2089-1x8x30	Spring	1x8x30	2

2		Nylon Pipe	Ф6x1	4

3	CB-6	Vitta Tie-in	M10x1	4

4 	CS-6	Clip Sleeve	Ф6	4

5		Tie-in 	M10x1	4

6	T1-6	Bushing	Ф6	4

7	C6266C04730	Connector		1

8	GB119-8x10	Pin	8x10	1

9	C6266C04731	Cover		1

10	GB819-M4x8	Cross Recessed Countersunk Head Screw	M4x8	2

11	C6266C04302Y	Bushing		1

12	C6266C04303Y	Plug		2

## Toolbox, Accessories, and Attachments

## Toolbox, Accessories, and Attachments

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	ZXOP-1A	3-Jaw Scroll Chuck (not shown)	10”, D1-8	1

2	ZXOP-2A	4-Jaw Independent Chuck (not shown)	13”, D1-8	1

3	C6250BC09103	Drive Plate		1

4	RNS-45-52	Round Nut Spanner	45-52	1

RNS-100-110	Round Nut Spanner	100-110	1

RNS-115-130	Round Nut Spanner	115-130	1

5	ZXOP-03N	Face Plate	16”	1

6	C6266C11103	Helical Gear	m3.75z14	1

7	ZXOP-MT7/ZXOP-08	Morse Reduction Sleeve *	MT7/MT5	1

8	ZX-OP-07N	Live Center *	MT5	1

9	ZX-OP-06	Dead Center *	MT5	1

10	1440R09703	Drive Pin (not shown)		2

11	ZXOP-05	Cam Wrench *		1

12	ZXOP-2B	Chuck Wrench *		1

13	ZXOP-04	Tool Post Wrench *		1

14	ZH-2517	Gap Bridge Pin Driver *		1

15	ZH-2518	Drift Key *		1

16		Hex Key Set *	2, 3, 4, 6, 8, 10, 12

one of each

17	ZH-2521	Leveling Bolt (ZH-2040/60/80) *	M20x80	6

ZH-2521	Leveling Bolt (ZH-20120) 	M20x80	8

18	ZH-2522	Hex Nut (ZH-2040/60/80) *	M20	6

ZH-2522	Hex Nut (ZH-20120) 	M20	8

19	ZX-01715	Leveling Pad (ZH-2040/60/80) *		6

ZX-01715	Leveling Pad (ZH-20120)		8

20	ZX-OP-14	Flat Blade Screw Driver *		1

21	ZX-OP-15	Cross Point Screw Driver *		1

22		Open End Wrench Set *	17-19	1		Open End Wrench Set *	19-22	1

23	ZX-OP-10	Touchup Paint Can (JET Gray) *		1

24	ZX-OP-09	Oil Gun *		1

25	GB70- M16x50	Hex Socket Head Cap Screw	M16x50	2

26	ZH-TBC	Tool Box Complete, ZH Lathes (includes items with asterisk * )

Electrical Components

FR2–FR3  KM1  KM2,KM3    QF1-QF3      7

HL         SA1           SB1         SB4

Electrical Diagram

Electrical Components-Parts List

#### Index	Part

#### No.	No.	Description	Model	Size	Qty.

M1.........	Y132M-4TH/B3	Main Motor	Y132M-4TH/B3	10HP, 3PH, 400V, 50HZ	1

M2 	ZX-CW04E	Coolant Pump	ZX-CW04E	1/2HP, 3PH, 400V	1

M3	YSS56BJ-G	Rapid Feed Motor	YSS5634	1/8HP, 3PH, 400V	1

QF	ZH-QF	Master Switch (serial #1601ZH0793 and lower)						JFD11	40A, 3P	1

QS	ZH-QS	Master Switch (serial #1601ZH0794 and higher)						V2C	40A, 3P	1

TC	ZH-TC	Control Transformer	JBK5-160VATH	400V/110V, 24V	1

FR2	ZH-FR2	Thermal Relay	3UA59	1.6-2.5A	1

FR3	ZH-FR3	Thermal Relay	3UA59	0.25-0.4A	1

KM1	ZX-KM3	A.C. Contactor	3TB43	Coil Voltage 24V，22A	1

KM2, KM3	ZX-KM2	A.C. Contactor	3TB40	Coil Voltage 24V，9A	2

QF1	ZH-QF1	Circuit Breaker (serial #1601ZH0794 and higher)					DZ47-63	3 Poles, 4A	1

QF2, QF3	ZH-QF2	Circuit Breaker (serial #1601ZH0794and higher)						DZ47-63	1 Pole, 3A	2

SQ1	ZH-SQ1	Door Switch	QKS8		1

SQ2	ZH-SQ2	Limit Switch	JW2A-11H/W1		1

SQ3	ZH-SQ3	Micro Switch	LXW5-11Q		1

SQ4	ZH-SQ4	Micro Switch	LXW5-11Q		1

SB1, SB3	ZH-SB1	Button	ZB2-BE102C	Red	2

SB2	ZH-SB2	Button	XB2-EA131	Green	1

SB4, SB5	ZH-SB4	Button	XB7-EA1C	Green	2

SA1	ZH-SA1	Turning Switch	ZB2-BE101C	Black	1

EL	ZH-EL	Work Lamp (serial #1601ZH0794and higher)

JC52B		1

HL	ZH-HL	Indicator Light	XB2EV163	24V, Green	1

1	C6266C18715-G	Electric Box Door			1

2	C6266C18713-G	Electric Box			1

4	C613218306	Copper Plate (for grounding)		1

5	JH9-2.5/4+1.5/31	Wiring Board			1

6	MS-705	Lock			1

7	C6140W18705	Small Shaft			2

C6140W18706	Pin Shaft			2

GB6170-M8	Hex Nut		M8	2

8	PG13.5-M20x1.5	Sheathed Wire Head		M20x1.5	1

9	AZ1-2004	Wiring Board			1

GB818-M4x6	Cross Recessed Pan Head Screw	M4x6	2

GB97.2-4	Flat Washer		4	2

10	GHB1340A18508-6	Warning Label			1

Digital Scale Units

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	Di Ma	Digital Scale Units (For GH-2040ZH only)	400×200×900	1Set

2	Di Ma	Digital Scale Units (For GH-2060ZH only)	400×200×1400	1Set

3	Di Ma	Digital Scale Units (For GH-2080ZH only)	400×200×1900	1Set

4	Di Ma	Digital Scale Units (For GH-20120ZH only)	400×200×2900	1Set

Flexible Stainless Wire Woven Tube

#### Index	Part

#### No.	No.	Description	Size	Qty.

1	ZH-TPDRO40	Flexible Stainless Wire Woven Tube for Protecting DRO Cable (for 2040ZH with DRO)			M16(1.5-3m	1

2	ZH-TPDRO60	Flexible Stainless Wire Woven Tube for Protecting DRO Cable (for 2060ZH with DRO)			M16(1.5-3.5m	1

3	ZH-TPDRO80	Flexible Stainless Wire Woven Tube for Protecting DRO Cable (for 2080ZH with DRO)			M16(1.5-3.9m	1

4	ZH-TPDRO120	Flexible Stainless Wire Woven Tube for Protecting DRO Cable (for 26120ZH with DRO)			M16(1.5-5m	1

5	ZH-TPCG	Flexible Stainless Wire Woven Tube for Protecting Chuck Guard Cable				M16(1.5M16(1.5-1.6m	1

# Text boxes

6

1

4

5

2

TC

10

QS

SB3

SB5

SB2

8

9